Example 3.2: Compute inductance per meter of each phase of a 3-phase transmission line with equilateral spacing. Assume

- The conductors are equally spaced, D, and have equal radii r.

- The currents sum to zero.

Solution: Let’s draw the situation below.

Recall that in the general case,

Since the currents sum to zero, we can apply to obtain:

Factoring ln(1/D) from the second and third terms:

Substituting ia=-(ib+ic), we get

Because the difference of logarithms is the logarithm of their ratio, we have:

So the inductance associated with phase a is