## Slide 1
Impact of Variability on Control Performance Metrics
James D. McCalley
Harpole Professor of Electrical & Computer Engineering
Iowa State University

## Slide 2: Impact of variability on control performance
Wind penetration is small now, so NERC says
decreasing freq gov charac β not due to wind,
  Source: “Comments Of The North American Electric Reliability Corporation Following September 23 Frequency Response Technical Conference,” Oct. 14, 2010
but…at higher wind penetrations,
  β will decrease if non-wind units with primary control are displaced by wind units without primary control;
  Reduced inertia and increased net load variability will cause greater frequency excursions.
Will higher wind penetrations degrade freq perf in terms of NERC’s Control performance metrics?
Each Balancing Authority shall achieve, as a minimum,
Requirement 1: CPS1 compliance of 100%
Requirement 2: CPS2 compliance of 90%
Potential requirements: BAAL and others….

## Slide 3
Control performance standards
Control Performance Standards CPS1 and CPS2 evolved from earlier metrics and were enacted by NERC in 1997 to evaluate a balancing area’s frequency control performance in normal interconnected power system operations.
The motivation underlying CPS is to ensure a targeted long term frequency control performance of the entire interconnection.
CPS measures each balancing area’s frequency control performance in achieving control objectives.
N.Jaleeli and ,L.VanSlyck, “Control performance standards and procedures for interconnected operation,” Electric Power Research Institute, Dublin, Ohio, Tech.Rep. TR-107813, Apr.1997.
N.Jaleeli and L.S.Vanslyk, “NERC’s new control performance standards. IEEE Trans. Power Syst.,” vol.14, pp.1092-1099, Aug.1999.

## Slide 4
Control performance standards
NERC Standard BAL-001-0.1a — “Real power balancing control performance,” http://www.nerc.com/files/BAL-001-0_1a.pdf.
CPS1
CPS2

## Slide 5
CPS1:a measure of a balancing area’s long term (12 mo) frequency performance.
Control objective - bound excursions of 1-minute average frequency error over 12 months in the interconnection.
Measures control performance by comparing how well a balancing area’s ACE performs in conjunction with the frequency error of the interconnection.
Ref: M. Terbrueggen, “Control Performance Standards” 2002
Average ACE, ΔF over 1 min to compute:
10B to give units of Hz.
ΔF is an interconnection measure. ΔPtie is a balancing area measure.
When ΔF<0, the interconnection needs generation, so desire BA to make
ΔPtie large  ACE>0 (helping). If ACE<0, it means BA is undergenerating  “hurting.”
So we want to see CP negative, large in mag.

## Slide 6
CPS1:a measure of a balancing area’s long term (12 mo) frequency performance.
Control objective - bound excursions of 1-minute average frequency error over 12 months in the interconnection.
Measures control performance by comparing how well a balancing area’s ACE performs in conjunction with the frequency error of the interconnection.
ε1 =target bound for 12 month of 1min avg freq error. e.g., 0.018Hz in EI, 0.228Hz in WECC, 0.020 Hz for ERCOT. Must be squared to normalize Hz2 in numerator.
Ref: M. Terbrueggen, “Control Performance Standards” 2002
Average ACE, ΔF over 1 min to compute:
Average CP 1min over 12 mo to compute:

## Slide 7
CPS1:a measure of a balancing area’s long term (12 mo) frequency performance.
Control objective - bound excursions of 1-minute average frequency error over 12 months in the interconnection.
Measures control performance by comparing how well a balancing area’s ACE performs in conjunction with the frequency error of the interconnection.
Problem: balancing area can grossly over- or under-generate (as long as it is opposite frequency error) and get very good CPS1, yet impact its neighbors with excessive flows (large ACEPtie,a>>Ptie,s).
Ref: M. Terbrueggen, “Control Performance Standards” 2002
Average ACE, ΔF over 1 min to compute:
Average CP 1min over 12 mo to compute:

## Slide 8
CPS2: measure of a balancing area’s ACE over all 10-minute periods in a month.
Control objective – limit ACE variations & bound unscheduled power flows between balancing areas.
Developed to address “problem” of previous slide.
BS=sum of B values for all control areas.
ε10 =target bound for 12 mo RMS of10-min avg freq error: e.g., 0.0057Hz in EI, 0.0073 for the WI and ERCOT.
In 2003, the 10Bs were ~ -5692 mw/0.1hz for EI, -1825 mw/0.1hz for WEEC, -920 mw/0.1Hz for ERCOT.
Requirement: |ACE10min |<
CPS2=100%-(Percent of 10 min periods in violation)>90%
L10 is max value within which ACE10min must be controlled

## Slide 9
Simulation System
Two Area System (Area A and Area B)
  Wind power is assumed in area A
Each area consists of 10 conventional units, with inertia and with speed governing
Based points are computed from net load forecast made 7.5 min ahead, with an assumed error of 1% for load and 4.5% for wind.
Wind penetration levels- 6%, 10%, 13%, 17%, 21%, 25% (Pw/Pnw) are considered (by capacity).
Wind is assumed to displace conventional units
Actual sec-by-sec p.u. value of load and of wind power data from one wind farm is used.
A
B
Wind units
Con units
Con units
C. Wang and J. McCalley, “Impact of Wind Power on Control Performance Standards,” under review, IEEE Trans on Pwr Sys.

## Slide 10
2 Area Simulation System
C. Wang and J. McCalley, “Impact of Wind Power on Control Performance Standards,” under review, IEEE Trans on Pwr Sys.

## Slide 11
Area 1 input
Area 2 input
Inputs for 2 Area Simulation System
The sec-by-sec generation levels in each case (PG1,RTED and PG2,RTED) are determined by linearly interpolating between their respective 5 minute load and wind forecasts.
C. Wang and J. McCalley, “Impact of Wind Power on Control Performance Standards,” under review, IEEE Trans on Pwr Sys.

## Slide 12
Study results
Normalized CPS1
Normalized CPS2
Case A: Area 1, Area 2 have same size.
Case B: Area 1 unchanged. Area 2 load and gen scaled up by 10.
Conclusions:
CPS1 and CPS2 deteriorates with increasing wind penetration.
The effect is larger for “smaller” interconnections.
C. Wang and J. McCalley, “Impact of Wind Power on Control Performance Standards,” under review, IEEE Trans on Pwr Sys.

## Slide 13
Study results
Measures to improve CPS1, CPS2:
M1: Increase primary frequency control capability in Area 1
M2: Increase the forecast accuracy of wind power
M3: Control wind power output to be no more than a band around forecasted value
M4: Combining control areas.
C. Wang and J. McCalley, “Impact of Wind Power on Control Performance Standards,” under review, IEEE Trans on Pwr Sys.

## Slide 14
Why Does CPS1 CPS2 Degradation Matter?
NERC penalties
Indication of greater frequency variability:
  Some loads may lose performance (induction motors)
  UFLS relay operation
  Volts per Hz relay operation
  Lifetime reduction of turbine blades
  Frequency dip may increase for given loss of generation
Indication of greater ACE variability:
  Increased inadvertent flows
  Increase control action of generators
Indication BA is “leaning on” others
QUESTION: Why do we divide the interconnection into BAs?
MOST IMPORTANT FACTORS

## Slide 15: Solutions to variability & uncertainty
Do nothing: fossil-plants provide reg & LF (and die ).
Improve forecasts (M2)
Increase control of the wind generation
  Control wind to band around forecasted value (M3)
  Provide wind with primary control
    Reg down (4%/sec), but spills wind following the control
    Reg up, but spills wind continuously
  Limit wind generation ramp rates
    Limit of increasing ramp is easy to do
    Limit of decreasing ramp is harder, but good forecasting can warn of impending decrease and plant can begin decreasing in advance
Increase non-wind MW ramping capability during periods of expected high variability using one or more of the below (M1):
  Conventional generation
  Load control
  Storage
  Expand control areas
Combine control areas (M4)
 | %/min | $/mbtu | $/kw | LCOE,$/mwhr
Coal | 1-5 | 2.27 | 2450 | 64
Nuclear | 1-5 | 0.70 | 3820 | 73
NGCC | 5-10 | 5.05 | 984 | 80
CT | 20 | 5.05 | 685 | 95
Diesel | 40 | 13.81 |  | 
15