EE 653 HW6, Spring Semester 2005, Dr. McCalley

- Consider the following 4 bus system with components and buses numbered as indicated and corresponding data provided in the accompanying table. The bus 3 load is 60 MVA and the bus 4 load is 40 MVA. Use max flow to compute the total system LOLP to within an accuracy of (2%.

| Component | Rating (MVA) | FOR |
| --- | --- | --- |
| Number | Description |  |  |
| 1 | Generator at bus 1 | 100 | 0.15 |
| 2 | Generator at bus 2 | 50 | 0.10 |
| 3 | Transmission line from bus1 to bus 3 | 110 | 0.10 |
| 4 | Transmission line from bus 1 to bus 2 | 50 | 0.05 |
| 5 | Transmission line from bus 2 to bus 4 | 100 | 0.15 |
| 6 | Transmission line from bus 3 to bus 4 | 50 | 0.05 |