U5 - Problem 7

We know that ambient temperature and wind speed are important in determining the current carrying capability of a transmission line. A transmission line owner wants to maximize its sale of capacity for a particular line in order to maximize its profits. However, it must decide how much capacity to sell on a day-ahead basis. Therefore it must predict temperature and wind. Let's denote the event "warm day" as event A and the event "windy day" as event B. The weather forecast indicates that the probability of a windy day is 0.80, the probability of a warm day is 0.30, and the probability of a warm and windy day is 0.28

- Are the events A and B independent?

- What is the probability of the event "windy day will be warm"?

- What is the probability of the event "warm day will be windy"?

- What is the probability of the event "windy and not warm"?

- What is the probability of the event "windy day will be not warm"?

- What is the probability of the event "not warm day will be windy"?

U5 - Problem 8

Of great interest to the electric power industry today is the detection of the "hot spot" temperature in power transformers. This is the temperature of the hottest part of the winding and is a function of many variables including loading and ambient temperature. A simplified approach assumes that if the hot spot temperature exceeds a certain level, the transformer will fail in one hour; otherwise it will not fail. The hot spot temperature may be approximated if both the oil temperature and the loading current are known.

We desire to predict transformer failure for a particular, rather low, loading current I. Let's denote the event "transformer failure" to be A. Let's also denote the event "oil temperature test indicates eminent failure" to be B. It is known that at the loading level I, =0.003 and that the oil temperature test has 2% false positives and 1% false negatives.

- What is ? (a is the complement of A)

- What is ?

- What is ?

- What is ?

- What is ?

- What is ?

- If, at this loading current I, the oil temperature test indicates the transformer will fail,

(i) What is the probability that the transformer will fail ?

(ii) What is the probability that the transformer will not fail ?

- Consider that the event A is "having cancer" and the event B is "positive test for cancer". What does the above result suggest about screening tests for diseases with low prevalence?

U6 - Problem 1

An engineer at a large industrial is looking for an energy seller to supply its electric energy needs. He has the names of five energy sellers, A, B, C, D, and E, and email addresses. He wants to know which ones have load following capability, so he sends them a message.

A and B are the only ones that have load following capability. If we assume that the order of reply is random, then we can define the number of replies necessary before a load following supplier is identified a the random variable Y, e.g., y=1 indicates that the first supplier to reply is a load following generator.

- Find and plot the probability mass function for Y. Hint: Evaluate  one at a time. The multiplication rule may help.

- Find and plot the cumulative distribution function for Y.

U7 - Problem 1

Suppose that the temperature T of a certain conductor has a uniform pdf in the range 40 to 60 degrees C. Then compute:

U7 - Problem 2

Let x denote the vibratory stress (psi) on a wind turbine blade for a particular wind speed y. Assume that the pdf for X is given by

Note that y is just a constant.

- Verify that  is a legitimate pdf

- Suppose y=100. What is the probability that x is

- less than 200 ?

- less than or equal to 200 ?

- Greater than 200 ?

- What is the probability that x is between 100 and 200 ?

- Give an expression for

U8 – Problem 9

- Two random variable, X and Y, are described by the following bi-variate probability density function:

fXY(x,y)	=6x2y	0.8736<x<1,   1<y<2

=0	otherwise

- Prove that this function is a valid pdf.

- Find both marginal distributions.

- Find the conditional pdf, fX(x|y).

- Compute Prob[X<0.9, Y< 1.3].

- Prove that X and Y are dependent, or prove that they are independent.

- Compute the mean value of X, (X.

U9 - Problem 3

George wants to buy electric energy. He can buy from company A, B, C, or D, but he must choose only one. George obtains past data on these four suppliers, and he then determines that the prices for some of them have been quite volatile, influenced by the state of the economy. George assesses this data and then forms the table below.

| Energy seller | Costs ($/MW-hr) |
| --- | --- |
|  | Recession | Stagnation | Inflation |
| A | 30 | 60 | 90 |
| B | 10 | 40 | 70 |
| C | 20 | 20 | 50 |
| D | 45 | 45 | 45 |
| Probability of economic state ( | 0.1 | 0.4 | 0.5 |

- Assuming that George simply wants to minimize his average costs over the long run, determine the expected costs for all energy suppliers. Select the supplier based on minimum expected cost.

- Assuming that George cannot afford any surprises and therefore wants to minimize his uncertainty, determine the standard deviation for each supplier. Select the supplier based on minimum variance (same as minimum standard deviation).

U13 Problem 1

- Prove that, for two random variables X1 and X2, with joint pdf f(x1,x2), the pdf of the random variable S=X1+X2 is given by

- Use the result of (a) to show that if X1 and X2 are independent, that